## Slide 1
Understanding UART Protocol and Architecture

## Slide 2
Introduction to UART Protocol
UART (Universal Asynchronous Receiver-Transmitter) is a protocol used for serial communication between two devices. It is a simple and widely used communication protocol that allows data to be transmitted and received between devices asynchronously.
UART Architecture
The UART architecture consists of a transmitter, a receiver, and a baud rate generator. The transmitter and receiver communicate through a common set of data lines, and the baud rate generator sets the speed at which data is transmitted and received.
Transmitter
Receiver
Baud Rate Generator
UART Architecture
UART Working
UART uses a start bit, data bits, parity bit, and stop bit to transmit and receive data. The start bit indicates the beginning of a byte, followed by the data bits, which contain the actual data being transmitted. The parity bit is used for error checking, and the stop bit indicates the end of a byte.
Start Bit
Data Bits
Parity Bit
Stop Bit
UART Data Transmission

## Slide 3
UART ARCHITECTURE
The UART architecture consists of two main components: the transmitter and the receiver.
Transmitter
The transmitter is responsible for converting parallel data into serial data and transmitting it through the communication channel. The transmitter consists of the following components:
Data Register: Stores the data to be transmitted.
Baud Rate Generator: Generates the clock signal for the transmitter and receiver to synchronize the data transmission.
Control Register: Configures the transmitter settings such as the number of data bits, parity, and stop bits.
Receiver
The receiver is responsible for receiving serial data from the communication channel and converting it into parallel data. The receiver consists of the following components:
Data Register: Stores the received data.
Baud Rate Generator: Generates the clock signal for the transmitter and receiver to synchronize the data transmission.
Control Register: Configures the receiver settings such as the number of data bits, parity, and stop bits.

## Slide 4
Data Transfer
UART transfers data in serial format, one bit at a time. It uses start and stop bits to indicate the beginning and end of a byte of data.
Data is transmitted LSB (Least Significant Bit) firstData is received MSB (Most Significant Bit) first
Baud Rate
The baud rate is the number of bits per second that are transmitted.
It is important to ensure that the transmitting and receiving devices have the same baud rate to ensure accurate data transfer.

## Slide 5
Start Bit
The transmission of data begins with a start bit, which is always a logic low (0).
Data Bits
The data bits are transmitted LSB first, followed by the MSB. The number of data bits can be configured to be 5, 6, 7, or 8 bits.
Parity Bit
The parity bit is optional and can be used for error detection. It can be configured to be even, odd, or none.
Stop Bit
The transmission of data ends with a stop bit, which is always a logic high (1).